## Slide 1
Dept. of Computer Science Engineering,
University of Hormuud
Lecturer: Abukar Mohamed Osman,
(Bsc in CS&IT , CCNA, WiMax, 3G, 4G , Msc in ÉTÉ)
CSE 5001: Embedded systems (3 Cr)
Lecture 03

## Slide 2: Basic peripherals

## Slide 3: Port
A port is a device
To receive the bytes from external peripheral(s) [or device(s) or processor(s) or controllers] for reading them later using instructions executed on the processor or
To send the bytes to external peripheral or device or processor using instructions executed on processor

## Slide 4
A Port connects to the processor using address decoder and system buses The processor uses the addresses of the port-registers for programming the port functions or modes, reading port status and for writing or reading bytes.

## Slide 5: Serial Transmission
Sender transmitted
Data is transmitted, on a single channel, one bit at a time one after another
- Much faster than parallel because of way bits processed (e.g. USB and SATA drives)
Receiver received
1
0
1
0
0
1
1
0

## Slide 6: Parallel Transmission
Receiver received
each bit has it’s own piece of wire along which it travels
- often used to send data to a printer
Sender transmitted
All bits are sent simultaneously
1
0
0
1
1
0
0
1

## Slide 7: Why Not use Parallel Instead of serial?
Due to inconsistencies on channels data arrives at different times
Because of the way it is transmitted packet switching cannot be used
The above two points makes parallel slower than serial and requires higher bandwidth.
Parallel transmissions are rarely used anymore

## Slide 8: IO Port Types
Synchronous Serial Input
Synchronous Serial Output
Asynchronous Serial UART input
Asynchronous Serial UART output

## Slide 9: Synchronous Serial Input
The sender along with the serial bits also sends the clock pulses SCLK (serial clock) to the receiver port pin. The port synchronizes the serial data input bits with clock bits. Each bit in each byte as well as each byte in synchronization.
Synchronization means separation by a constant interval or phase difference. If clock period = T, then each byte at the port is received at input in period = 8T.

## Slide 10: Cont…
The bytes are received at constant rates. Each byte at input port separates by 8T and data transfer rate for the serial line bits is (1/T) bps. [1bps = 1 bit per s]
On same input line − when clock pulses either encode or modulate serial data input bits suitably.
Receiver detects the clock pulses and receives data bits after decoding or demodulating.

## Slide 11
On separate input line − When a separate SCLK input is sent, the receiver detects at data-input is 1 or 0 and saves the bits in an 8-bit shift register. The processing element at the port (peripheral) saves the byte at a port register from where the microprocessor reads the byte.

## Slide 12: Master output slave input (MOSI) and Master input slave output (MISO)
MOSI when the SCLK is sent from the sender to the receiver and slave is forced to synchronize sent inputs from the master as per the inputs from master clock.
MISO when the SCLK is sent to the sender (slave) from the receiver (master) and slave is forced to synchronize for sending the inputs to master as per the master clock outputs.
Synchronous serial input is used for inter processor transfers, audio inputs and streaming data inputs.

## Slide 13: Half Duplex
Half duplex means as follows: at an instant communication can only be one way (input or output) on a bi-directional line. An example of half-duplex mode─ the talk can only in the half duplex way mode.

## Slide 14: Full Duplex
Full duplex means that at an instant, the communication can be both ways.
An example of the full duplex
asynchronous mode of communication

## Slide 15: Two Modes of communication between the devices and computer system
Full Duplex – Both devices or device and computer system simultaneously communicate each other
Half Duplex – Only one device can communicate with another at an instance

## Slide 16: Three ways of communication between the ports or devices
Synchronous
Iso-synchronous
Asynchronous

## Slide 17: Synchronous Communication
When a byte (character) or a frame (a collection of bytes) in of the data is received or transmitted at the constant time intervals with uniform phase differences, the communication is called as synchronous. Bits of a full frame are sent in a prefixed maximum time interval.

## Slide 18: First characteristics of synchronous communication
1. Bytes (or frames) maintain a constant phase difference, which means they are synchronous,
i.e. in synchronization. No permission of sending either the bytes or the frames at the random time intervals, this mode therefore does not provide for handshaking during the communication interval ─ This facilitates fast data communication at pre-fixed bps.

## Slide 19: Second characteristics of synchronous communication
2. A clock marking at a certain rate has always to be there for transmitting serially the bits of all the bytes (or frames) serially. The transmitter generally transmits the clock rate information

## Slide 20: Asynchronous Communication
Clocks of the receiver and transmitter independent, unsynchronized, but of same frequency and variable phase differences between bytes or bits of two data frames, which may not be sent within any prefixed time interval

## Slide 21: Two characteristics of asynchronous communication
1. Bytes (or frames) need not maintain a constant phase difference and are asynchronous, i.e., not in synchronization. There is permission to send either bytes or frames at variable time intervals─ This facilitates in-between handshaking between the serial transmitter port and serial receiver port

## Slide 22
2. Though the clock must indicate a certain rate always has to be there to transmit the bits of a single byte (or frame) serially

## Slide 23: Clock Features
The transmitter does not transmit (neither separately nor by encoding using modulation) along with the serial stream of bits any clock rate information in the asynchronous communication and receiver clock thus is not able to maintain identical frequency and constant phase difference with transmitter clock

## Slide 24: Communication Protocols
A protocol is a standard adopted, which tells the way in which the bits of a frame must be sent from a device (or controller or port or processor) to another device or system
[Even in personal communication we follow a protocol – we say Hello! Then talk and then say good bye!]

## Slide 25
A protocol defines how are the frame bits:
1) sent− synchronously or Iso synchronously or asynchronously and at what rate(s)?
2) preceded by the header bits?
3) How the receiving device address communicated so that only destined device activates and receives the bits?
[Needed when several devices addressed though a common line (bus)]

## Slide 26
4) How can the transmitting device address defined so that receiving device comes to know the source when receiving data from several sources?
5) How the frame-length defined so that receiving device know the frame-size in advance?

## Slide 27
6) Frame-content specifications −Are the sent frame bits specify the control or device configuring or commend or data?
7) Are there succeeding to frame the trailing bits so that receiving device can check the errors, if any in reception before it detects end of the frame ?

## Slide 28
A protocol may also define:
8) Frame bits minimum and maximum length permitted per frame
9) Line supply and impedances and line-Connectors specifications

## Slide 29
Parallel port one bit Input
Parallel one bit output
Parallel Port multi-bit Input
Parallel Port multi-bit Output

## Slide 30: Protocols in embedded network devices
Internet appliances application protocols and Web protocols ─HTTP (hyper text transfer protocol), HTTPS (hyper text transfer protocol Secure Socket Layer), SMTP (Simple Mail Transfer Protocol), POP3 (Post office Protocol version 3), ESMTP (Extended SMTP),

## Slide 31: File transfer Protocols in embedded devices network
TELNET (Tele network),
FTP (file transfer protocol),
DNS (domain network server),
IMAP 4 (Internet Message Exchange
Application Protocol)

## Slide 32: Programming
An essential part of any embedded system design.
Processor and memory-sensitive instructions: Program codes may be written in assembly
Most of codes: Written in a high level language (HLL), ‘C’, ‘C++’ or Java

## Slide 33: Advantage of using high level language (HLL) for Programming
Code reusability─ A function or routine can be repeatedly used in a program.
Standard library functions─ For examples, the mathematical functions and delay ( ), wait ( ), sleep ( ) functions
Use of the modular building blocks

## Slide 34
Short Development Cycle─ Bottom-up design
Sub-modules are designed first for specific and distinct set of actions, then the modules and finally integration into complete design.
First code the basic functional modules and then build a bigger module and then integrate into the final system

## Slide 35
Use of Type Checking
Type checking during compilation makes the program less disposed to errors.
Example─ type checking on a char data type variable (a character) does not permit subtraction, multiplication and division.

## Slide 36
Use of Control Structures, loops and Conditions
Control Structures and loops
• Examples─ while, do-while, break and for Conditional Statements examples if, if- else, else - if and switch - case) Makes tasks simple for the program flow design

## Slide 37
Use of Objects
Objects bind the data fields and methods to manipulate those fields Objects reusability Provide inheritance, method overloading, overriding and interfacing Many other features for ease in programming